## Slide 1: Homework solutions
EE3143

## Slide 2
Resistive circuits
Problem 1
Use KVL and Ohms law to compute voltages va and vb .
+
+
+
+
v2
-
-
-
-
v1
From Ohms law:
v1=8kW*i1=8[V]
v2=2kW*i2=-2[V]
Form KVL:
va=5[V]-v2=7[V]
vb=15[V]-v1-va=0[V]

## Slide 3
Resistive circuits
Problem 2
Write equations to compute voltages v1 and v2 , next find the current value of i1
From KCL:
50 mA=v1/40+(v1-v2)/40
and
100 mA=v2/80+(v2-v1)/40
Multiply first equation by 40:
2=v1+v1-v2=2v1-v2
From second equation:
8=v2+2(v2-v1)=3v2-2v1 add both sides:
10=2v2 => v2=5 [V], v1=1+v2 /2=3.5[V]
i1= (v1-v2)/40=-1.5/40=37.5 [mA]
50 mA
100 mA
i1
i1
v2
v1

## Slide 4
Thevenin & Norton
Problem 3: Find Thevenin and Norton equivalent circuit for the network shown.
I1
N2
I2
vt
N1
From KVL

## Slide 5
Thevenin & Norton
I1
N2
I2
Isc
N1
From KVL

## Slide 6
Thevenin & Norton
Note: Negative vt indicates that the polarity is reversed and as a result this circuit has a negative resistance.
+
_
Vt=-6 V
RTh=-1.33Ω
A
B
Thevenin Equivalent
In=4.5 A
RTh=-1.33Ω
A
B
Norton Equivalent
RTh=vt/Isc=-1.33Ω

## Slide 7
Problem 4: Find the current i and the voltage v across LED diode in the circuit shown on Fig. a) assuming that the diode characteristic is shown on Fig. b).
Draw load line. Intersection of load line and diode characteristic is the i and v across LED diode: v ≈ 1.02 V and i ≈ 7.5 mA.

## Slide 8
Problem 5: Sketch i versus v to scale for each of the circuits shown below. Assume that the diodes are ideal and allow v to range from -10 V to +10 V.
(a)
Diode is on for v > 0 and R=2kΩ.
+
v
_
2kΩ
i
In a series connection voltages are added for each constant current

## Slide 9
Problem 5: Sketch i versus v to scale for each of the circuits shown below. Assume that the diodes are ideal and allow v to range from -10 V to +10 V.
(b)
Due to the presence of the 5V supply the diode conducts only for v > 5, R = 1kΩ
+
v
_
1kΩ
i
+
_
5V
First combine diode and resistance then add the voltage source

## Slide 10
(c)
Diode B is on for v > 0 and R=1kΩ.
Diode A is on for v < 0 and R=2kΩ.
+
v
_
2kΩ
i
1kΩ
A
B
Problem 5: Sketch i versus v to scale for each of the circuits shown below. Assume that the diodes are ideal and allow v to range from -10 V to +10 V.

## Slide 11
(d)
Diode D is on for v > 0 and R=1kΩ.
Diode C is on for v < 0 and R=0Ω.
+
v
_
i
1kΩ
C
D
Problem 5: Sketch i versus v to scale for each of the circuits shown below. Assume that the diodes are ideal and allow v to range from -10 V to +10 V.

## Slide 12
Problem 6 Sketch the transfer characteristic (vo versus vin) for the circuit shown in the figure below. Assume that the diode is ideal.
Modeling a piecewise characteristic of a device
1kΩ
i
v
i
-
+
v
vx
In a parallel connection currents are added for each constant voltage

## Slide 13
Problem 6 Sketch the transfer characteristic (vo versus vin) for the circuit shown in the figure below. Assume that the diode is ideal.
Modeling a piecewise characteristic of a device
1kΩ
i
v
i
-
+
v
vx
In a parallel connection currents are added for each constant voltage

## Slide 14
Problem 6 Add the voltage source.
Modeling a piecewise characteristic of a device
1kΩ
i
-
+
v
In a series connection voltages are added for each constant current
+
vo
_
+
Vin
-
v
i
vin

## Slide 15
Problem 6 Add the voltage source.
Modeling a piecewise characteristic of a device
1kΩ
i
-
+
v
+
vo
_
+
Vin
-
2kΩ
In a parallel connection currents are added for each constant voltage
v
i
vin

## Slide 16
Problem 6 Add the voltage source.
Modeling a piecewise characteristic of a device
1kΩ
i
-
+
v
+
vo
_
+
Vin
-
2kΩ
In a parallel connection currents are added for each constant voltage
v
i
vin

## Slide 17
Ia
4V
-
+
5V
-
+
(a)
S
D
G

## Slide 18
Ib
1V
-
+
3V
-
+
(b)
D
S
G

## Slide 19
Ic
4V
+
-
5V
-
+
(c)
G
D
S
c

## Slide 20
Id
3V
-
+
1V
-
+
(d)
G
S
D

## Slide 21
1.8 MΩ
2 kΩ
0.2 MΩ
sin(200πt)
+
_
Zin
+20 V
D
G
S
Loop 1
Problem 8: Consider the amplifier shown below.
a) Find vGS(t). Assume that the coupling capacitor is a short circuit for the ac signal and an open circuit for the dc.
Soln (a): In loop 1 the 1.8 MΩ and 200 kΩ resistors act as voltage divider.
The voltage drop across 200 kΩ resistor is the dc voltage VGSQ
VGSQ = 20*0.2/2=2 V
Treating the capacitor as short for ac signals, we have
VGS =2 + sin(200πt)

## Slide 22
b) If the FET has Vt0 = 1V and K = 0.5 mA/V2, sketch its drain characteristics to scale for VGS = 1, 2, 3, and 4 V.
c) Draw the load line for the amplifier on the characteristics.
d) Find the values of VDSQ, VDSmin, and VDSmax.
To obtain the drain characteristics apply the following equations

## Slide 23
b) Plot shows the drain characteristics for VGS = 1, 2, 3, and 4 V.
c) To get the load line apply KVL to loop 2:
20 – 2 kΩ*iD(t) = VDS(t)
The red line in the plot is the load line.
1.8 MΩ
2 kΩ
0.2 MΩ
sin(200πt)
+_
Zin
+20 V
D
G
S
Loop 2

## Slide 24
d) VDSQ, VDSmin, and VDSmax are the points at which the load line intersects the drain characteristics for VGS = 2 V, 3 V and 1 V respectively.
VDSQ = 19 V
VDSmin = 16 V
VDSmax = 20 V
d) Find the values of VDSQ, VDSmin, and VDSmax.

## Slide 25: Problem 9: Consider the common source amplifier shown below. Assume NMOS transistor has the following parameters: 𝐾𝑃=60 𝜇𝐴∕𝑉2, 𝐿=5 𝜇𝑚, 𝑊=100 𝜇𝑚, 𝑟𝑑=∞, and 𝑉𝑡𝑜=1.5 𝑉. a) Find the values of 𝐼𝐷𝑄, 𝑉𝐷𝑆𝑄and 𝑔𝑚
R1 =
72 kΩ
R2 =
28 kΩ
+
vin
_
C1
+10 V
C2
RL=
1 kΩ
+
vo
_
RD = 5 kΩ
The 72 kΩ and 28 kΩ resistors act as a voltage divider. The voltage drop across 28 kΩ resistor is the dc voltage VGSQ is equal to

## Slide 26: Problem 9 b): - Assuming that the coupling capacitors are short circuits for the ac signal, determine the following: voltage gain, input resistance and output resistance.
R1 =
72 kΩ
R2 =
28 kΩ
+
vin
_
C1
+10 V
C2
RL=
1 kΩ
+
vo
_
RD = 5 kΩ

## Slide 27: Problem 10: - Consider the common source amplifier shown below. Assume NMOS transistor has the following parameters: 𝐾𝑃=75 𝜇𝐴∕𝑉2 , 𝐿=10 𝜇𝑚, 𝑊=400 𝜇𝑚, 𝑟𝑑=∞, and 𝑉𝑡𝑜=1 𝑉. a) If Rin = 250 kΩ, find the values for R1 and R2 to achieve 𝐼𝐷𝑄=2 𝑚𝐴.
R1
R2
v(t)
+
_
C1
+15 V
RS =
0.5 kΩ
C2
RL =
5 kΩ
R
+
vin(t)
_
+
vo
_
RD =
2 kΩ
Rin

## Slide 28
R1
R2
v(t)
+
_
C1
+15 V
RS =
0.5 kΩ
C2
RL =
5 kΩ
R
+
vin(t)
_
+
vo
_
RD =
2 kΩ
Rin
We have:
Given:
Solve for R1:

## Slide 29
We have Rin = 250 kΩ and R1 = 1.19 M Ω
Solve for R2:
b) Determine the voltage gain

## Slide 30: Problem BJT P1: It has been found that in the circuit below VE = 1V. If VBE = -0.6V, determine: VB, IB, IE, IC, β, and α.
VE = 1V
IE
IC
IB
VBE = -0.6V
VB
Soln (a): From KVL:
From KVL:
Ohm’s law:

## Slide 31: Problem BJT P2: - For the circuit below assume both transistors are silicon-based with β = 100. Determine: a) IC1, VC1, VCE1. b) IC2, VC2, VCE2.
RB1
IB1
VBE1
IC1 + IB2
IC2
VBE2
RC1
RC2
RE2
IE2
VC1
VCE1
VCE2
IC1
IB2
Soln:
Assume VBE= VBE1 =VBE2 = 0.7V
Part (a): - Apply KVL along the path (red line).

## Slide 32
RB1
IB1
VBE1
IC1 + IB2
IC2
VBE2
RC1
RC2
RE2
IE2
VC1
VCE1
VCE2
IC1
IB2
Part (a) contd.: - Apply KVL along the path (red line).
We know that
substituting we get

## Slide 33
RB1
IB1
VBE1
IC1 + IB2
IC2
VBE2
RC1
RC2
RE2
IE2
VC1
VCE1
VCE2
VC2
VE2
IC1
IB2
Part (b): - Apply KVL along the path (red line).

## Slide 34: Problem BJT P3: - Design the bias circuit (find RC and RB) to give a Q-point of IC = 20µA and VCE = 0.9V if the transistor current gain βF = 50 and VBE = 0.65V. What is the Q-point if the current gain of the transistor is 125?
IC = 20µA
IB
VCE = 0.9V
VBE = 0.65V
Soln: Apply KVL along the path (red line).

## Slide 35
IC = 20µA
IB
VCE = 0.9V
VBE = 0.65V
Soln contd.: (find RC and RB) to give a Q-point of IC = 20µA and VCE = 0.9V.
Apply KVL along the path (red line).

## Slide 36
IC
IB
VCE
VBE = 0.65V
IC + IB
Soln contd.: Find the Q-point if the current gain, βF = 125. We have RC=29.41kΩ, and RB=625kΩ, from previous calculations.
Apply KVL along the path (red line).

## Slide 37
IC
IB
VCE
VBE = 0.65V
IC + IB
Soln contd.: Apply KVL along the path (red line).
The Q-Point is:

## Slide 38: Problem OP-AMP P1: - Consider the op-amp circuit shown below. If 𝑣𝑖𝑛 (𝑡) = 6 + 9𝑐𝑜𝑠(500𝜋𝑡), calculate the value of R2 required to generate a output, vo(t), with zero DC component. What is the resulting output voltage?
Soln: The circuit shown is that of a differential amplifier. We can use superposition theorem to solve for the output voltage: connect inputs to ground (0 V), one at a time, and solve for output voltage.
-
+
+
vin(t)
_
+
5V
_
+
vo(t)
_
R2
5 kΩ
Va
Vb
From summing point constraints: Va = Vb
From KVL2
From KVL1 and Ohms law
Therefore
iin
KVL1
KVL2

## Slide 39
-
+
+
vin(t)
_
+
5V
_
+
vo(t)
_
R2
5 kΩ
Va
Vb
If DC component of vo is zero,
Multiplying by 5kW on both sides and solving for R2,
R2 = 25 kΩ
Then the output is 𝑣o = - 45𝑐𝑜𝑠(500𝜋𝑡),

## Slide 40: Problem OP-AMP P2: - Consider the op-amp circuit shown below. Assume the maximum output voltage of the op-amp ranges from – 12 V to + 12 V; the maximum output current magnitude is 25 mA; and the slew-rate limit is 1.5 V/µs. If 𝑣𝑖𝑛 (𝑡)=𝑣𝑚𝑠𝑖𝑛(𝜔𝑡), R1 = 5 kΩ, and R2 = 25 kΩ. a) Find the full-power bandwidth of the op-amp.
-
+
+
vin(t)
_
+
vo(t)
_
R2
R1
RL
Soln: The full-power bandwidth of the op-amp is given by
Slew-rate, SR = 1.5 V/µs;
maximum output amplitude,Vom = 12 V.

## Slide 41: b) Find the peak output voltage possible without distortion for the following cases:
Case a: Frequency of 5 kHz and RL = 20 Ω
  Soln.: The current limit of the op-amp limits the peak output voltage. Since RL is very small compared to R2 the current through R2 can be neglected. Thus the peak output voltage is given by
Case b: Frequency of 5 kHz and RL = 2.5 kΩ
  Soln.: Vom = 12 V (The maximum voltage that the op-amp can achieve.)
Case c: Frequency of 50 kHz and RL = 2.5 kΩ
  Soln.: The slew-rate limit of the op-amp limits the peak output voltage.

## Slide 42: Problem Logic Gates P1: - Express the following functions in canonical SOP form. (Hint: Draw the truth table for each one first.).
Soln:-
a) F(A, B, C) = (A + B’)C’ + A’C
F(A, B, C) = AC’ + B’C’ + A’C=
A’B’C’+A’B’C+A’BC+AB’C’+ABC’
b) F(X, Y, Z) = (X + Y’)(X’ + Z) + ZY’
F(X, Y, Z) = XX’ + XZ + X’Y’ + Y’Z + ZY’
F(X, Y, Z) = XZ + X’Y’ + Y’Z
= =X’Y’Z’+X’Y’Z+XY’Z+XYZ
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
X | Y | Z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 43
c) F(A, B, C, D) = AB’C + A’BC’D + A’BCD’ + B’D’
F(A, B, C, D) =AB’CD+AB’CD’+ A’BC’D + A’BCD’ + +AB’C’D’+A’B’CD’+A’B’C’D’
d) F(W, X, Y, Z) = WX’ + Z’(Y’ + W’) + W’Z’Y’
F(W, X, Y, Z) = WX’ + Y’Z’ + W’Z’ + W’Z’Y’
F(W, X, Y, Z) = W’X’YZ’+W’X’YZ’+WX’YZ’+WX’Y’Z’+
+WX’YZ+WX’Y’Z+WXY’Z’+W’XY’Z’+W’XYZ’
Karnaugh Map instead of truth table:
 |  |  | C |  | 
 |  |  |  | D | 
 |  | 1 | 1 |  | 
A |  | 1 | 1 | 1 | 
 | B |  |  |  | 
 |  |  | 1 |  | 1
 |  |  | Y |  | 
 |  |  |  | Z | 
 |  | 1 | 1 |  | 
W |  | 1 | 1 | 1 | 1
 | X | 1 |  |  | 
 |  | 1 | 1 |  | 

## Slide 44: Problem Logic Gates P2: - Realize AND, OR and NOT functions using: a) NOR, b) NAND
Soln. a:- Using NOR Gates
Soln. b:- Using NAND Gates

## Slide 45: Problem Logic Gates P3: - a) Use Karnaugh-map to find the SOP form of the following function: F = BC’D’ + BC’D + A’C’D’ + BCD’ + A’B’CD’
Soln:-
F = BC’D’ + BC’D + A’C’D’ + BCD’ + A’B’CD’
SOP: F = BD’ + BC’ + A’D’
 |  | C |  |  | 
 | 1 | 1 |  |  | 
A |  |  |  |  | 
 | 1 | 1 |  | 1 | B
 | 1 | 1 |  | 1 | 
 |  |  | D |  | 

## Slide 46: Problem Logic Gates P3: - b) Find the minimum POS form of the function above and draw a logic circuit representing the same.
Soln:-
For minimum POS – Minimize the logic function F’ and take inverse. That is consider locations with zero (0) and then invert the result.
POS: F = (B + D’) . (A’ + B) . (C’ + D’)
 |  | C |  |  | 
 | 1 | 1 | 0 | 0 | 
A | 0 | 0 | 0 | 0 | 
 | 1 | 1 | 0 | 1 | B
 | 1 | 1 | 0 | 1 | 
 |  |  | D |  |